## Slide 1: LEDs as Sensors
Paul H. Dietz, PhD
Philantic, LLC.
Redmond, WA
Ginger Alford, PhD
SMU Lyle School of Engineering
Dallas, TX

## Slide 2: Prerequisites
Played with Arduino before
  Made an LED blink on and off
At least a vague understanding of voltage and current
  Analogies to water pressure (voltage) and flow (current)

## Slide 3: What’s an LED?
Light Emitting Diode
  Emits light proportional to the forward current flow
  It is a diode
Source: https://en.wikipedia.org/wiki/Light-emitting_diode#/media/File:LED,_5mm,_green_(en).svg
(flag)
(longer lead)
(shorter lead)
+
Anode
-
Cathode

## Slide 4: Ideal Diode Model
No current flows until voltage reaches (forward voltage)
Above , acts like a short so generally need some way to limit the current
I
V

## Slide 5: Powering an LED
Need to limit the current
  Typically use a resistor
Example:
  =1.5V
  R=220
  I = (5V-1.5V)/220  15.9mA

## Slide 6: Digital I/O Pins Ideal Model

## Slide 7: Driving an LED from the Arduino Uno
I/O pins can connect to power or ground (or neither – input)
  Two ways of controlling an LED
    Right is inverted (LOW is on)
  Pin 13 is setup switching power to a resistor and LED on board

## Slide 8: Task #1: Blink an LED
_01_Blink_Pin13_LED.ino

## Slide 9: Arduino Blink (Using on-board LED)
_01_Blink_Pin13_LED.ino
// Blink Pin 13 LED
#define LED 13 // On-board LED is on Pin 13
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED, OUTPUT);
}
void loop() {
digitalWrite(LED, HIGH); // turn the LED on (HIGH is the voltage level)
delay(250); // wait for 1/4 second
digitalWrite(LED, LOW); // turn the LED off by making the voltage LOW
delay(250); // wait for 1/4 second
}
Arduino UNO has on-board LED on Pin 13

## Slide 10: Add an External LED
Provided LED with pre-soldered resistor on Anode (+) side
Connect resistor to 13 and other lead to GND
No need to change the code

## Slide 11: Stuff They Didn’t Tell You About LEDs
LED are photodiodes
  Notably Pointed out by Forrest Mims in the 1970’s
  LEDs generate photo current when exposed to light
A reverse biased LED has capacitance

## Slide 12: About Capacitors
A capacitor is a device which stores charge
  Current flowing into a capacitor increases the voltage across it
  Charge flowing out of a capacitor decrease the voltage across it
For a reverse biased LED, the photocurrent removes charge from (discharges) the junction capacitance
Current
Voltage
+
-

## Slide 13: Stuff They Didn’t Tell You About Input Pins
When used as an input:
  Exceptionally low leakage current
    UNO processor (ATMEGA348P) specifies <1uA leakage
    Actual leakage is much less than 1uA
    Close to ideal model
Logic Threshold :
  Varies with supply, temp, device
    Stable in the short term
  Usually less than half supply
  ATMEGA348 specifies as 1.5-3V on a 5V supply
Works like a comparator to some unknown, slowly changing voltage
High
Vin
Low

## Slide 14: In This Section: Sense and Emit Light
Goal: Sense and emit light using capacitance of LED
  Make it look simultaneous by switching back and forth quickly
    Flicker fusion is around 50Hz
Circuit: Reverse bias the LED using digital pins 3 and 4
Software: three programs:
  _02_GraphLight.ino
  _03_SenseAndLight .ino
  _04_AutoLight.ino
Experiment: Use flashlight to increase light on LED. Observe variations in time to discharge capacitance.

## Slide 15: Using the UNO to Measure Light with an LED
Connect LED-resistor across I/O pins 3 and 4 as shown
Reverse bias the LED
  This charges the junction capacitance
Change one of the pins to an input
Let the photocurrent discharge the capacitance
  Rate depends on light level
See how long it takes before input switches logic level

## Slide 16: Reverse Bias

## Slide 17: Photocurrent Discharge
Input
(volts)
Time
Slope depends
on Iphoto – more
Light, more current,
faster discharge
Switch from LOW to INPUT
Photocurrent causes voltage on input to rise from low to high
(which is discharging the cap because it is decreasing the voltage
across the cap)
Reverse Bias

## Slide 18: Task #2: Graph Light Level Using Serial Plotter
_02_GraphLight.ino
Tools Menu -> Serial Plotter
  Set baud rate to 250000
Use flashlight.
Observe in plotter how long it takes for capacitance to discharge

## Slide 19: Task #3: Sense Light and Emit Light Loop
_03_SenseAndLight .ino
After discharge timing is done, switch the pins to forward bias the LED
Light for 1ms
Reset back to reverse bias

## Slide 20: I/O Sequence

## Slide 21: Task #4: AutoLight
_04_AutoLight.ino
Reverse bias
Let go
Wait a fixed amount of time
Check once to see if threshold passed
Light LED if dark
Wait a fixed amount of time

## Slide 22: In This Section: Sense Temperature and Wind
Goal: To make an LED you can blow out
Circuit: Measure the forward voltage drop of LED using an Arduino analog input
Software: three programs:
  _05_GraphHotLED.ino
  _06_GraphHotLED256 .ino
  _07_BlowOutLED.ino
Experiment: Blow on the LED and observe variations in forward voltage in plotter.

## Slide 23: Pre-wired 0402 LED for Fast Thermal Response

## Slide 24: Measuring

## Slide 25: Close-Up of the Wiring

## Slide 26: Sensing Temperature with an LED
Diodes are frequently used to sense temperature on chip
At a fixed current, forward voltage drop of a silicon diode has a temperature coefficient of ~ -2mv/C
LEDs are diodes, but use different materials
Forward
Voltage
Temperature
Forward voltage drop decreases with increasing
temperature

## Slide 27: Forward Voltage Drop vs Temperature
“All LEDs exhibit forward voltage variation as junction temperature changes. The temperature coefficient depends from junction type. InGaAlP LEDs (Yellow and Amber Red) have a coefficient of between -3.0 mV/K to -5.2 mV/K, and the InGaN LEDs (Blue, Verde Green, and White) have a coefficient of between –3.6 mV/K and -5.2 mV/K. (Golden Dragon LWW5SG)”
https://www.onsemi.com/pub/Collateral/TND328-D.PDF

## Slide 28: Task #5: Graph Hot LED
_05_GraphHotLED.ino
Turn on the LED
Measure the voltage drop on the LED

## Slide 29: Task #6: Graph Hot LED with Averaging
_06_GraphHotLED256.ino
Need to increase the resolution of the measurement
Average across many readings
No need to do the division
  Just report the sum

## Slide 30: Task #7: A Hot LED Anemometer
_07_BlowOutLED.ino
LED self heats when on
Temperature raises above ambient
When wind blows on LED, it cools
rises when LED temperature drops
Detect the sudden rise to sense when someone blows on the LED

## Slide 31: Detecting the Temperature Drop
Compare the current with an earlier one to see if it rose
  Store previous readings in circular buffer
Forward
Voltage
Time
Compare current with earlier
Trigger when:
(t) - > MINJUMP
(t)
(t-Δ)
Δ

## Slide 32: LEDs as Interfaces
Output
  Human-readable output
  Machine-readable output
Input
  Measure light levels
    Detect human gestures
    Receive data from devices
  Measure Temperature
    Measure ambient temperature
  Hot LED Anemometer
    Measure wind speed
      Detect puffs
    Measure wind direction
      Use multiple Hot LEDs and baffles
    Detect puffs location
Talk to a widget’s LED with a phone app
Build interfaces for the disabled
Make expressive musical instruments
Create an electronic birthday cake with candles you can blow out

## Slide 33: Refs and Acknowledgements
Interesting References
  Mims, Forrest M., III, Siliconnections: Coming of Age in the Electronic Era, McGraw-Hill, New York, NY, 1986.
  Filippo, R.; Taralli, E.; Rajteri, M., “LEDs: Sources and Intrinsically Bandwidth-Limited Detectors”, Sensors, 2017. https://www.ncbi.nlm.nih.gov/pmc/articles/PMC5539727/
  Dietz, P.H.; Yerazunis, W.S.; Leigh, D.L., "Very Low-Cost Sensing and Communication Using Bidirectional LEDs", ACM International Conference on Ubiquitous Computing (UbiComp), October 2003. http://www.merl.com/publications/TR2003-35
  Jeff Han’s touch LED array: https://mrl.nyu.edu/~jhan/ledtouch/index.html
  Scott E. Hudson. 2004. Using light emitting diode arrays as touch-sensitive input and output devices. In Proceedings of the 17th annual ACM symposium on User interface software and technology (UIST '04). ACM, New York, NY, USA, 287-290. DOI: https://doi.org/10.1145/1029632.1029681
Acknowledgements
  Rita Kambil – Made up the parts kits for this workshop
  James Scott @ Microsoft Research – unpublished work on new LED interfaces